## Slide 1: Computer-Aided Design تراشه های منطقی برنامه پذیر
Mahdi Aminian
Some slides courtesy of:
CAD slides, Dr. Saheb Zamani
allaboutcircuits.com

## Slide 2: Digital Circuits
Acronyms
SPLD = Simple Programmable Logic Device
PAL = Programmable Array Logic
CPLD = Complex PLD
FPGA = Field Programmable Gate Array
ASIC = Application Specific IC
Logic
Standard
Logic
ASIC
Programmable
Logic Devices
(FPLDs)
Gate
Arrays
Cell-Based
ICs
Full Custom
ICs
CPLDs
SPLDs
(e.g., PALs)
FPGAs
Microprocessor
& RAM
Common Resources
Configurable Logic Blocks (CLB)
  Memory Look-Up Table (LUT)
  AND-OR planes
  Simple gates
Input / Output Blocks (IOB)
  Bidirectional, latches, inverters, pullup/pulldowns
Interconnect or Routing
  Local, internal feedback, and global

## Slide 3: Full Custom

## Slide 4: ASIC (Application Specific IC)
ASIC: Application-Specific Integrated Circuits
Semi-Custom ASIC:
  Standard Cells
    عناصر در رديفها چيده مي شوند
    پورتها در بالا و پايين سلولها (تکنولوژي جديد: روي سلولها)
  Gate Array
    آرايه اي از سلولهاي مشابه
  PLD (Programmable Logic Device)

## Slide 5: سلول های استاندارد
Adder
NAND
MUX
Wires

## Slide 6: Mixed
Full custom & Standard cells
RAM/ROM
Row based Control Logic
Row based CPU

## Slide 7: Gate Array (Uncommitted)
Using a prefabricated chip with active devices like NAND-gates
Later, interconnected according to a custom order by adding metal layers in the factory environment

## Slide 8: Gate Array (Committed)
MPGA: mask-programmed gate array
MPLD: mask-programmed logic device
A base of pre-designed transistors
Customized wiring during manufacturing process
→ Each design requires custom masks for wiring
Mask-making costs

## Slide 9: Programmable Logic Device
A programmable logic device or PLD is an electronic component used to build digital circuits
Unlike a logic gate, which has a fixed function, a PLD has an undefined function at the time of manufacture
Before the PLD can perform in a circuit it must be programmed

## Slide 10: Digital Technology Tradeoffs
S
SPLD
SSI/MSI
semicustom technologies
standard components
CPLD FPGA
Gate
Array
Std.
Cell
Full
Custom

## Slide 11: “Programmable”

## Slide 12: “Programmable”?
One time programmable
  Fuses
  (destroy internal links with current)
  Anti-fuses (grow internal links)
  PROM
Reprogrammable
  EPROM
  EEPROM
  Flash
  SRAM → volatile
}
non-volatile

## Slide 13: Antifuse
جريان برنامه ريزي بالا  عايق ONO را ذوب مي کند  اتصال دايم.
به علت کوچکي، PLD هاي آنتي فيوز ظرفيت بسيار بالايي دارند.

## Slide 14: Antifuse
مزايا:
  عدم نياز به حافظه ي خارجي.
  مساحت بسيارکم (تقريبا هم اندازه با viaي سيمهاي فلزي).
  قابليت اطمينان بسيار بالا
    (TDDB: Time-Dependent Dielectric Breakdown) حدود 40 سال.
  مقاومت کم در حالت روشن (در طي زمان هم کم مي ماند).
  خازن پارازيتي بسيار کمتر.
  امنيت بالاي طرح در برابر سرقت.
  توان مصرفي بسيار کمتر.
اشکالات:
  عدم امکان برنامه ريزي مجدد.
  برنامه ريزي آن نياز به مدار اضافي دارد (بايد ولتاژ و جريان بالا ايجاد کند).

## Slide 15: Programmable ROM (PROM)
First ones had fusible links
High voltage would blow out links
Fast to program
Single use

## Slide 16: UV EPROM
Erasable PROM
Common technologies used UV light to erase complete device
  Took about 10 minutes
Holds state as charge in very well insulated areas of the chip
Nonvolatile for several (10?) years

## Slide 17: EEPROM
Electrically Erasable PROM
Similar technology to UV EPROM
Erased in blocks by higher voltage
Programming slower than reading
Some called flash memory
  Digital cameras, MP3 players, BIOS
  Limited life
  Some support individual word write, some block
  Has a boot block that is carefully protected

## Slide 18: EPROM/EEPROM/Flash
ولتاژ برنامه ريزي بالا  محبوس شدن الکترونها  Vdd نمي تواند ترانزيستور را روشن کند
EEPROM: باز گرداندن الکترونها با ميدان الکتريکي (ظرفيت کمتر از EPROM).

## Slide 19: SRAM
SRAM
SRAM Cell

## Slide 20: SRAM
مزايا:
  برنامه ريزي مجدد سريع.
  برنامه ريزي on-chip به دفعات نامحدود.
   prototyping در داخل سيکل طراحي
  کارخانه ي سازنده مي تواند همه ي مسيرها را با reprogram کردن FPGA تست کند ( کاربر، آي سي کاملا تست شده را مي گيرد و نيازي به ايجاد الگوهاي تست و مدارهاي DFT ندارد).
اشکالات:
  مساحت (اشکال اصلي): 5 ترانزيستور براي هر سلول SRAM + يک ترانزيستور براي سوييچ.
  نياز به حافظه ي خارجي non-volatile (داراي مدار حسگر power-on است براي initialization).
  امنيت کم طرح در برابر سرقت (intellectual property)
  توان مصرفي بالاي سلول هاي SRAM (حتي وقتي که برنامة آن تغيير نمي کند).

## Slide 21: Programmable Logic Device (PLD)

## Slide 22: Three FPLD Types
Simple Programmable Logic Device (SPLD)
  LSI device (Less than 1000 logic gates)
  PLA or PAL
  Fixed internal routing, deterministic propagation delays
Complex Programmable Logic Device (CPLD)
  VLSI device (Higher logic capacity than SPLDs)
  Multiple SPLDs onto a single chip
  Programmable interconnect
Field Programmable Gate Array (FPGA)
  VLSI device (Higher logic capacity than CPLDs)
  An array of logic blocks
  Large number of gates, user selectable interconnection, delays depending on design and routing
  A high ratio of flip-flops to logic resources

## Slide 23: SPLD

## Slide 24: Simple PLD (SPLD)
Popular SPLD Architecture Types
  Programmable Logic Array, PLA
  Programmable Array Logic, PAL
  General Array Logic, GAL
  others
Architecture Differences
  AND versus OR implementation
  Programmability (e.g., EE)
  Fundamental logic block

## Slide 25: PLA & PAL
A PLA has complete flexibility of its sum-of-products groupings.
Programmable Logic Array
A PAL has limits on the arrangement of its sum-of-products groupings.
Programmable Array Logic

## Slide 26: SPLD - PLA
SPLDs are good alternative to using SSI and MSI devices
  Especially if re-programmable
B
A
C
D
F
G
H
J
ABC
AD
AD
BD
B
ABC
F = ABC’ + AD + A’D
G = ABC + ABC’ + A’D
H = ABC + BD
J = B + AD

## Slide 27: SPLD - PAL
P
1
P
2
I
1
I
2
I
3
P
3
P
4
Implement the following:

## Slide 28: SPLD - PAL
P
1
P
2
x
1
x
2
x
3
P
3
P
4
AND plane
P4
P3
P2
P1
f1
f2

## Slide 29: SPLD - PAL
An actual PAL device
PAL16L8
  32 input AND gates
  up to 8 output functions

## Slide 30: PAL Outputs
Typical PALs have:
  from 10 to 20 inputs
  from 2 to 10 outputs
  from 2 to 8 AND gates driving each OR gate
  often include D flip-flops
f
1
To AND plane
D
Q
Clock
Select
Enable
Flip-flop
MUX output is “fed back” to the AND plane.

## Slide 31: PAL Product Terms
This looks like an AND gate with one input. It is actually many more:
B
B’
A
A’
C
C’
H’
H
Drawn with a single line (above) to save space.
B B’A A’ C C’ D D’ I I’ J J’ E E’ F F’ K K’GG’H H’
P

## Slide 32: PAL Example
A
B
C
D
G
H
I
J
P
P’ = A’BGH’ + CD’ + HIJ + BG’H

## Slide 33: CPLD

## Slide 34: CPLD
PALs and GALs are available only in small sizes
  equivalent to a few hundred logic gates
For bigger logic circuits, complex PLDs or CPLDs can be used.
CPLDs contain the equivalent of several PALs/GALs
  linked by programmable interconnections
  all in one integrated circuit (IC)
CPLDs can replace thousands, or even hundreds of thousands, of individual logic gates
  increased integration density

## Slide 35: CPLD

## Slide 36: Programmable Interconnect Array
Consists of connectors that run throughout the CPLD to connect the macrocells in each LAB
The PIA also connects the AND gate and other elements of the macrocells