## Slide 1: Computer-Aided Design تراشه های منطقی برنامه پذیر
Mahdi Aminian
Some slides courtesy of:
CAD slides, Dr. Saheb Zamani
allaboutcircuits.com

## Slide 2: Digital Circuits
Acronyms
SPLD = Simple Programmable Logic Device
PAL = Programmable Array Logic
CPLD = Complex PLD
FPGA = Field Programmable Gate Array
ASIC = Application Specific IC
Logic
Standard
Logic
ASIC
Programmable
Logic Devices
(FPLDs)
Gate
Arrays
Cell-Based
ICs
Full Custom
ICs
CPLDs
SPLDs
(e.g., PALs)
FPGAs
Microprocessor
& RAM
Common Resources
Configurable Logic Blocks (CLB)
  Memory Look-Up Table (LUT)
  AND-OR planes
  Simple gates
Input / Output Blocks (IOB)
  Bidirectional, latches, inverters, pullup/pulldowns
Interconnect or Routing
  Local, internal feedback, and global

## Slide 3: FPGA

## Slide 4: Field Programmable Logic Array (FPGA)
2-D array of logic blocks and flip-flops with programmable interconnections
User can configure
  Intersections between the logic blocks
  The function of each block
FPGAs are usually programmed after being soldered down to the circuit board, in the same way as larger CPLDs
In most larger FPGAs the configuration is volatile, and must be re-loaded into the device whenever power is applied or different functionality is required

## Slide 5: FPGA vs. MicroController

## Slide 6: FPGA vs. MicroController

## Slide 7: Logic Blocks (LB)
Granularity: is the hardware abstraction level. According to granularity, two types of Blocks :
Fine Grain Logic Blocks
Coarse Grain Logic Blocks
Purpose: to implement combinational and sequential logic functions.
Logic blocks can be implemented by:
  Transistor pairs
  Multiplexers
  Look up tables( LUT)
  Wide fan-in AND-OR structure.

## Slide 8: Look-Up Table (LUT)

## Slide 9: Look-Up Table (LUT)
Output of SRAM gives the logic output
k-input logic function =2^k size SRAM
K-input LUT gives 2^2^k logic functions

## Slide 10: Implementation of Logic Functions using LUT

## Slide 11: Implementation of Logic Functions using LUT-3 & MUX

## Slide 12: Implementation of a 3-input logic function using 4-input LUT

## Slide 13: Effects of Granularity on FPGA Density and Performance
Tradeoff
  Granularity increase → Blocks less
  More Functional Blocks → more area
Area is normally measured by total number of bits needed to implement the design. So look the example

## Slide 14: Programmable Switch Matrix (PSM)

## Slide 15: SRAM-Based FPGA
Programmable Lookup Tables (LUTs)
Programmable routing structure

## Slide 16: FPGA ArchitecturE

## Slide 17: FPGA Development
FPGAs evolved from Gate Arrays
Parallel with development of CPLDs

## Slide 18: FPGA
Silicon wafer containing XC4010E 10,000 gate FPGAs.
die showing 20 by 20 array of logic elements and interconnect.

## Slide 19: FPGA Architecture

## Slide 20: Routing Criteria
Routability
سرعت: تعداد سوييچها در مسير
فضا.
  منابع اتصالي کم  کاهش امکان پياده سازي مدار مورد نظر
  منابع اتصالي زياد  اتلاف مساحت و کاهش بخش هاي منطقي

## Slide 21: Terms Definition
Wire Segment: قطعه سيمي که به يک سوييچ برنامه پذير منتهي شده است.
  يک يا چند سوييچ مي تواند به يک wire segment وصل شده باشد.
Track (شيار): دنباله اي از يک يا چند wire segment در امتداد يک خط.
Channel: گروهي از Trackهاي موازي.
Connection Block: اتصال از وروديها و خروجيهاي يک LC به wire segmentهاي کانال.
Switch Block: اتصال بين wire segmentهاي افقي و عمودي.

## Slide 22: Routing Structure Example

## Slide 23: Spartan Logic Cell
Spartan Logic Cell

## Slide 24: Cyclone FPGA
SRAM-based

## Slide 25: Cyclone V Architecture
Gigabit Transceiver Blocks

## Slide 26: Cyclone V Architecture

## Slide 27: ALM Structure

## Slide 28: Advanced FPGA Architectures
The Xilinx Zynq-7000 AP SoC product line provides scalable performance and configuration serving a wide range of applications needs. The combination of the ARM® dual-core Cortex™-A9 MPCore™ processing system and 7 series programmable logic provides a computing platform. Zynq-7000 AP SoC is ideal for solutions requiring advanced system control combined with sophisticated signal processing.