## Slide 1: Computer-Aided Design Design Cycle
Mahdi Aminian
Some slides courtesy of:
CAD slides from Dr. Saheb Zamani
Xilinx & Altera products documentations

## Slide 2: FPGA vs. ASIC Design Flow

## Slide 3: چرخه ي طراحي براي FPLDها
Design Entry
  Schematic Netlist
  HDL
  Waveform
  State Diagram

## Slide 4: چرخه ي طراحي براي FPLDها
مزايا:
  کوتاه شدن پروسه ي طراحي.
نوآوري بيشتر (پروسه ي طراحي به مراحل بالاتر رفتاري منتقل مي شود) (تشابه با زبانهاي سطح بالا)
Debug طرح بسيار آسانتر و سريعتر.
  مانند سيکل برنامه نويسي:
تغييرات در طرح بسيار آسانتر.
  بعضي شرکتها نسخه هاي جديد سخت افزار خود را روي CD يا از طريق اینترنت در اختيار مشتري خود قرار مي دهند تا EPROM را مجددا برنامه ريزي کند.
کامپايل
اجرا
برنامه نويسي
ويرايش
کامپايل
شبيه سازي
ورود طرح
ويرايش
سنتز
شبيه سازي
ويرايش

## Slide 5: FPGA and Embedded Design
http://www.xilinx.com/training/free-video-courses.htm#ASIC

## Slide 6: Entry – HDL Coding
HDL allows us to describe the functionality of a logic circuit in a language that is:
  Easy to understand
  Easy to share
  Hide complicated implementation details
Designer more concerned about the design functionality than the detailed circuit design

## Slide 7: Simulation by Testbenches
After HDL coding, the code has to be tested using “Testbenches” (Verification)
Simulation Tools
  Modelsim (Mentor Graphics)
  Simulators of Synthesis Tools

## Slide 8: Synthesis
Synthesis Tool:
  Analyzes a piece of HDL code and converts it into optimized logic gates
  This conversion is done according to the “language semantics”
→ We have to learn these language semantics, i.e., VHDL code
Why using synthesis tools?
  It is an important tool to improve designers’ productivity to meet today’s design complexity
  If a designer can design 150 gates a day, it will take 6666 man’s day to design a 10-million gate design, or almost 20 years for 10 designers! This is assuming a linear grow of complexity when design gets bigger

## Slide 9: Synthesis Tools
Input
  HDL Code
  “Technology Library” file
  Constraint file (Timing, area, power, loading requirement, optimization Alg.)
Output
  A gate-level “Netlist” of the design
  Timing files (.sdf)

## Slide 10: Synthesis Example
A 2-to-1 Multiplexer (2x1 Mux)

## Slide 11: Synthesis Tool
Infer logic and state elements
Perform technology-independent optimizations
  e.g., logic simplification, state assignment
Map elements to the target technology
Perform technology-dependent optimizations
  Multi-level logic optimization
  Choose gate strengths to achieve speed goals

## Slide 12: Implementation for FPGA

## Slide 13: Application of HDLs
VHDL به عنوان زبان مستندسازي (توصيف فرمال و بدون ابهام).
سنتز: تبديل (اتوماتيك يا دستي) يك توصيف به توصيفي با جزئيات بيشتر

## Slide 14: Concepts of HDL
Execution of Statements:
  Sequential
  Concurrent
اجرای دستورات:
  ترتیبی
  همزمان (موازی)

## Slide 15: Concepts of HDL
  Abstraction: طرح را مي توان در سطوح مختلفي از جزئيات توصيف كرد:
      براي مدلسازي، سطوح بالا كافي است.
      براي سنتز، ممكن است جزئيات بيشتري لازم باشد.
  Modularity: مي توان بلوك بزرگ پيچيده را به بلوكهاي كوچكتر تقسيم كرد و براي هر بخش يك مدل نوشت.
  Hierarchy: تشكيل يك درخت سلسله مراتبي
      هر كدام از نودها ممكن است در سطح متفاوتي از abstraction توصيف شده باشد.

## Slide 16: Modeling Capability