## Slide 1: Computer-Aided Design VHDL Syntax
Mahdi Aminian
Some slides courtesy of:
“Hardware Systems Modeling”, A. Vachoux, EPFL
“VHDL”, Dan Solarek, University of Toledo
CAD slides from Dr. Saheb Zamani

## Slide 2: VHDL - Overview
Very High Speed Integrated Circuit Hardware Description Language
  Modeling of digital systems
  Concurrent and sequential statements
International Standards
  IEEE Std 1076-1987
  IEEE Std 1076-1993, 2000, 2002, …
علاوه بر استانداردهاي خالص, تلاشهايي براي استاندارد كردن عوامل مربوط به VHDL انجام گرفته است:
  پكيج هاي
    Std_logic_1164
    Numeric_bit
    Numeric_std
  زيرمجموعة قابل سنتز: استاندارد 1076.6
  VHDL-AMS 1076.1

## Slide 3: Abstraction Levels in IC Design
  VHDL براي سطح layoutمناسب نيست.

## Slide 4: VHDL Structural Elements
Entity: Interface
Architecture: Implementation, behavior
Configuration: Structure, hierarchy
Process: Sequential Execution
Package: Components (Modular design), Utilities (data types, constants, subprograms)
Library: Group of compiled units, object code

## Slide 5: Design Library

## Slide 6: Design File

## Slide 7: VHDL Key Idea
A key idea in VHDL is to define the interface of a hardware module while hiding its internal details.
  A VHDL entity is simply a declaration of a module’s inputs and outputs, i.e., its external interface signals or ports.
  A VHDL architecture is a detailed description of the module’s internal structure or behavior.
entity
architecture
interface
interface

## Slide 8: VHDL Interface - Ports
You can think of the entity as a “wrapper” for the architecture
  hiding the details of what’s inside
  providing “ports” to other modules
entity
architecture
output port
.
.
.
.
.
.

## Slide 9: VHDL Conceptual Model
VHDL actually allows you to define multiple architectures for a single entity
it also provides a configuration management facility that allows you to specify which architecture to use during a particular synthesis run
entity
architecture 1
architecture 2
configuration

## Slide 10: VHDL Design Units

## Slide 11: Entity
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end entity HALFADDER;
Interface description
No behavior/implementation definition
entity ADDER is port( A, B: in integer range 15 to 0; SUM: out integer range 15 to 0; CARRY: out bit ); end ADDER;
Linking via port signals
  data types
  signal width
  signal direction
in bit_vector (3 downto 0); out bit_vector (3 downto 0);

## Slide 12: Entity Port Modes
in:
  signal values are read-only
out:
  signal values are write-only
  multiple drivers
buffer:
  similar to out
  signal values may be read, as well
  only 1 driver
inout:
  bidirectional port

## Slide 13: General
---------------------------------- -- Example VHDL Code -- ---------------------------------- signal mySignal: bit; -- an example signal MYsignal <= '0', -- start with '0' '1' AFTER 10 ns, -- and toggle after '0' after 20 ns, -- every 10 ns '1' afTer 30 ns;
Statements are terminated by ';' (may span multiple lines)
List delimiter: ','
Signal assignment: '<='
User defined names:
  letters, numbers, underscores
  start with a letter
Comments: '--' until end of line

## Slide 14: VHDL Identifiers (Names)
Basic identifier
  starts with a letter
  made up of letters, numbers, and underscore “_” character
  cannot end with an underscore
  case-insensitive: MY_Signal_Name = my_signal_name
Extended Identifier
  any text within 2 backslashes
  e.g., \2FOR$\ \-23signal\ etc.
  case is significant: \COUNT\ not equal to \count\, and \FRAMUS\ not equal to basic identifier FRAMUS
  Not often used – not necessarily supported in synthesis !!
not recommended

## Slide 15: Identifiers
mySignal_23 -- normal identifier rdy, RDY, Rdy -- identical identifiers vector_&_vector -- X : special character last of Zout -- X : white spaces idle__state -- X : consecutive underscores 24th_signal -- X : begins with a numeral open, register -- X : VHDL keywords
(Normal) Identifier
  Letters, numerals, underscores
\mySignal_23\ -- extended identifier \rdy\, \RDY\, \Rdy\ -- different identifiers \vector_&_vector\ -- legal \last of Zout\ -- legal \idle__state\ -- legal \24th_signal\ -- legal \open\, \register\ -- legal
Extended Identifier:
  Enclosed in back slashes
  Case sensitive
  Graphical characters allowed
  May contain spaces and consecutive underscores
  VHDL keywords allowed

## Slide 16: Architecture
entity HALFADDER is port( A, B: in bit; SUM, CARRY: out bit); end HALFADDER; architecture RTL of HALFADDER is begin SUM <= A xor B; CARRY <= A and B; end architecture RTL;
Implementation of the design
Always connected with a specific entity
  one entity can have several architectures
  entity ports are available as signals within the architecture
Contains concurrent statements

## Slide 17: Architecture Structure
architecture EXAMPLE of STRUCTURE is subtype DIGIT is integer range 0 to 9; constant BASE: integer := 10; signal DIGIT_A, DIGIT_B: DIGIT; signal CARRY: DIGIT;
begin DIGIT_A <= 3; SUM <= DIGIT_A + DIGIT_B; DIGIT_B <= 7; CARRY <= 0 when SUM < BASE else 1; end EXAMPLE ;
Declarative part:
  data types
  constants
  intermediate signals
  component declarations
  ...
Statement part (after 'begin'):
  signal assignments
  processes
  component instantiations
  concurrent statements: order not important
   Simulator recalculates sum any time an operand changes
Port is a kind of signal.

## Slide 18: Four Classes of Data Objects
Constant
  Holds a single value of a given type – cannot change.
Signal
  Holds a LIST of values of a given type.
  Present value + a set of possible future values
  New values can be assigned at some future time – not now!
  Signals have ATTRIBUTES: [signal’attribute]
Variable
  Holds a single value of a given type.
  New value of same type can be “assigned” – (instantly)
File
  Contains a sequence of values of one or more types.
  Usually read or written to using procedures
  For simulation – not synthesis
analogous to a “wire”

## Slide 19: Data Types
Scalar Types
  Enumerated : a list of values
  Integer
  Floating Point
  Physical : with units, for physical quantities
Composite Types
  Array (all of same type)
  Record (can be different types)
Access Type
File Type

## Slide 20: Enumerated Types
CHARACTER – one of the ASCII set
BOOLEAN – can be FALSE or TRUE
BIT – can be ‘0’ or ‘1’ (note single quotes)
STD_LOGIC
  Has NINE legal values:
  ‘U’, ‘X’, ‘0’, ‘1’, ‘Z’, ‘W’, ‘L’, ‘H’, ‘-’
Example Declarations
  Type CAR_STATE is (back, stop, slow, medium, fast);
  Subtype GO_KART is CAR_STATE range stop to medium;
  Type DIGIT is (‘0’, ‘1’, ‘2’, ‘3’, ‘4’, ‘5’, ‘6’, ‘7’, ‘8’, ‘9’ );
IEEE std_logic_1164 package

## Slide 21: Logic Data Representation

## Slide 22: Time Representation: Type time

## Slide 23: Arrays
An Array of type BIT is called a BIT_VECTOR
  signal MYSIG : IN BIT_VECTOR( 0 to 3);
An Array of type STD_LOGIC is called a STD_LOGIC_VECTOR
  signal yourSIG : OUT STD_LOGIC_VECTOR( 31 downto 0);
A STRING is a character array
  constant GREETING: STRING := “Hello!”;

## Slide 24: Signal

## Slide 25: Signal Assignment Statement

## Slide 26: Process Statement
entity AND_OR_XOR is port (A,B : in bit; Z_OR, Z_AND, Z_XOR : out bit); end AND_OR_XOR; architecture RTL of AND_OR_XOR is begin A_O_X: process (A, B) begin Z_OR <= A or B; Z_AND <= A and B; Z_XOR <= A xor B; end process A_O_X ; end RTL;
Contains sequentially executed statements
Only within an architecture
Several processes run concurrently
Execution is suspended either via
  sensitivity list (contains trigger signals), or
  wait-statements
Signal values don’t change until suspension

## Slide 27: Process Activation Control

## Slide 28: Process
ابزارهاي سنتز معمولاً ليست حساسيت را ناديده مي گيرند
براي مدارهاي ترکيبي همة وروديها بايد در ليست قرار گيرند تا نتيجة شبيه سازي قبل از سنتز با سخت افزار سنتز شده مطابقت داشته باشد.
براي مدارهاي ترتيبي، فقط clock و وروديهاي آسنکرون (reset, preset) در ليست قرار گيرند.

## Slide 29: VHDL Communication Model
Processes are concurrent statements
  Several processes
  run in parallel
  linked by signals in the sensitivity list
Link to processes of other entity/architecture pairs via entity interface

## Slide 30: Packages
Collection of definitions, datatypes, subprograms
Reference made by the design team
Any changes are known to the team immediately
  same data types ("downto vs. to")
  extended functions for all
  clearing errors for all

## Slide 31: Packages
پکيجها در دو بخش نوشته مي شوند:
  Package Header: شامل اعلان subprogram prototypeها، data typeها، ...
  Package Body: شامل پياده سازي subprogramها
کامپايل را آسان مي کند: فقط header بايد خوانده شود تا تطبيق کد VHDL جاري با تعاريف اعلانهاي قبلي مشخص شود.

## Slide 32: Package Declaration & Body

## Slide 33: Library
:

## Slide 34: Modeling Combinational Logic: 1-Bit Full Adder

## Slide 35: 1-Bit Full Adder: Dataflow Models