## Slide 1: Computer-Aided Design FSM Implementation
Some slides courtesy of:
“Hardware Systems Modeling”, A. Vachoux, EPFL
CAD slides from Dr. Saheb Zamani
Mahdi Aminian

## Slide 2: FSM
FSM ?
FSM Design ?
FSM Implementation ?

## Slide 3: Finite State Machines & VHDL
One- , two- or three-processes
State Encoding
FSM Types
  Medvedev
  Moore
  Mealy
  Registered Output

## Slide 4: Enumeration Types
architecture EXAMPLE of ENUMERATION is type T_STATE is (RESET, START, EXECUTE, FINISH); signal CURRENT_STATE, NEXT_STATE : T_STATE ; signal TWO_BIT_VEC : bit_vector(1 downto 0); begin -- valid signal assignments NEXT_STATE <= CURRENT_STATE; CURRENT_STATE <= RESET; -- invalid signal assignments CURRENT_STATE <= "00"; CURRENT_STATE <= TWO_BIT_VEC; end EXAMPLE;
Designers may define their own types
  enhanced readability (commonly used to describe the states of a state machine)
  limited legal values
Synthesis tools map enumerations onto a suitable bit pattern automatically.

## Slide 5: One-Process FSM
FSM_FF: process (CLK, RESET) begin if RESET='1' then STATE <= START ; elsif CLK'event and CLK='1' then case STATE is when START => if X=GO_MID then STATE <= MIDDLE ; end if ; when MIDDLE => if X=GO_STOP then STATE <= STOP ; end if ; when STOP => if X=GO_START then STATE <= START ; end if ; when others => STATE <= START ; end case ; end if ; end process FSM_FF ;

## Slide 6: Two-Process FSM
FSM_LOGIC: process ( STATE , X) begin case STATE is when START => if X=GO_MID then NEXT_STATE <= MIDDLE ; end if ; when MIDDLE => ... when others => NEXT_STATE <= START ; end case ; end process FSM_LOGIC ;
FSM_FF: process (CLK, RESET) begin if RESET='1' then STATE <= START ; elsif CLK'event and CLK='1' then STATE <= NEXT_STATE ; end if; end process FSM_FF ;

## Slide 7: How Many Processes?
Structure and Readability
  Asynchronous combinatory, synchronous storing elements => 2 processes
  Graphical FSM (without output equations) resembles one state process => 1 process
Simulation
  Error detection easier with two state processes due to access to intermediate signals. => 2 processes
Synthesis
  2 state processes can lead to smaller generic net list and therefore to better synthesis results (depends on synthesizer but in general, it is closer to hardware) => 2 processes

## Slide 8: State Encoding
type STATE_TYPE is ( START, MIDDLE, STOP ) ; signal STATE : STATE_TYPE ;
State encoding responsible for safety of FSM
START -> " 00 " MIDDLE -> " 01 " STOP -> " 10 "
Default encoding: binary
START -> " 001 " MIDDLE -> " 010 " STOP -> " 100 "
Speed optimized default encoding: one hot
Note: unsafe FSM!

## Slide 9: Encoding of CASE Statement
type STATE_TYPE is (START, MIDDLE, STOP) ; signal STATE : STATE_TYPE ; · · · case STATE is when START => · · · when MIDDLE => · · · when STOP => · · · when others => · · · end case ;
Adding the "when others" choice
Not necessarily safe; some synthesis tools will ignore "when others" choice

## Slide 10: Extension of Type Declaration
type STATE_TYPE is (START, MIDDLE, STOP, DUMMY) ; signal STATE : STATE_TYPE ; ··· case STATE is when START => ··· when MIDDLE => ··· when STOP => ··· when DUMMY => ··· -- or when others end case ;
Adding dummy values
Only for binary encoding
Advantages:
  Safe FSM after synthesis
{2 log2(# of states) - n} dummy states (n=20 => 12 dummy states)
Changing to one hot coding => unnecessary hardware (n=20 => 12 unnecessary Flip Flops)

## Slide 11: Hand Coding
subtype STATE_TYPE is std_ulogic_vector (1 downto 0) ; signal STATE : STATE_TYPE ; constant START : STATE_TYPE := "01"; constant MIDDLE : STATE_TYPE := "11"; constant STOP : STATE_TYPE := "00"; ··· case STATE is when START => ··· when MIDDLE => ··· when STOP => ··· when others => ··· end case ;
Defining constants
Control of encoding
Safe FSM
Portable design
Disadvantage:
More effort (especially when design changes)

## Slide 12: FSM: Medvedev
Two Processes
architecture RTL of MEDVEDEV is ... begin REG: process (CLK, RESET) begin -- State Registers Inference end process REG ; CMB: process (X, STATE) begin -- Next State Logic end process CMB ; Y <= S ; end RTL ;
The output vector resembles the state vector: Y = S
One Process
architecture RTL of MEDVEDEV is ... begin REG: process (CLK, RESET) begin -- State Registers Inference with Logic Block end process REG ; Y <= S ; end RTL ;

## Slide 13: Medvedev Example (2-Process)
architecture RTL of MEDVEDEV_TEST is signal STATE,NEXTSTATE : STATE_TYPE ; begin REG: process (CLK, RESET) begin if RESET='1' then STATE <= START ; elsif CLK'event and CLK='1' then STATE <= NEXTSTATE ; end if ; end process REG;
CMB: process (A,B,STATE) begin case STATE is when START => if (A or B)='0' then NEXTSTATE <= MIDDLE ; end if ; when MIDDLE => if (A and B)='1' then NEXTSTATE <= STOP ; end if ; when STOP => if (A xor B)='1' then NEXTSTATE <= START ; end if ; when others => NEXTSTATE <= START ; end case ; end process CMB ; -- concurrent signal assignments for output (Y,Z) <= STATE ; end RTL ;

## Slide 14: Medvedev Example Waveform
(Y,Z) = STATE => Medvedev machine

## Slide 15: FSM: Moore
Three Processes
architecture RTL of MOORE is ... begin REG: -- Clocked Process CMB: -- Combinational Process OUTPUT: process (STATE) begin -- Output Logic end process OUTPUT ; end RTL ;
The output vector is a function of the state vector: Y = f(S)
Two Processes
architecture RTL of MOORE is ... begin REG: process (CLK, RESET) begin -- State Registers Inference with Next State Logic end process REG ; OUTPUT: process (STATE) begin -- Output Logic end process OUTPUT ; end RTL ;

## Slide 16: Moore Example
architecture RTL of MOORE_TEST is signal STATE,NEXTSTATE : STATE_TYPE ; begin REG: process (CLK, RESET) begin if RESET='1' then STATE <= START ; elsif CLK'event and CLK='1' then STATE <= NEXTSTATE ; end if ;
end process REG ;
Since outputs depend only on the current state, no signals other than STATE appears in the sensitivity list.
CMB: process (A,B,STATE) begin case STATE is when START => if (A or B)='0' then NEXTSTATE <= MIDDLE ; end if ; when MIDDLE => if (A and B)='1' then NEXTSTATE <= STOP ; end if ; when STOP => if (A xor B)='1' then NEXTSTATE <= START ; end if ; when others => NEXTSTATE <= START ; end case ; end process CMB ; -- concurrent signal assignments for output Y <= ‘1’ when STATE=MIDDLE else ‘0’ ; Z <= ‘1’ when STATE=MIDDLE or STATE=STOP else ‘0’; end RTL ;

## Slide 17: Moore Example Waveform
(Y,Z) changes simultaneously with STATE  Moore machine

## Slide 18: FSM: Mealy
The output vector is a function of the state vector and the input vector: Y = f(X,S)
Three Processes
architecture RTL of MEALY is ... begin REG: -- Clocked Process CMB: -- Combinational Process OUTPUT: process (STATE, X) begin -- Output Logic end process OUTPUT ; end RTL ;
Two Processes
architecture RTL of MEALY is ... begin MED: process (CLK, RESET) begin -- State Registers Inference with Next State Logic end process MED ; OUTPUT: process (STATE, X) begin -- Output Logic end process OUTPUT ; end RTL ;

## Slide 19: Mealy Example
architecture RTL of MEALY_TEST is signal STATE,NEXTSTATE : STATE_TYPE ; begin
REG: · · · -- clocked STATE process CMB: · · · -- Like Medvedev and Moore Examples OUTPUT: process (STATE, A, B) begin case STATE is when START => Y <= '0' ; Z <= A and B ; when MIDLLE => Y <= A nor B ; Z <= '1' ; when STOP => Y <= A nand B ; Z <= A or B ; when others => Y <= '0' ; Z <= '0' ; end case; end process OUTPUT; end RTL ;

## Slide 20: Mealy Example (Another Code)
architecture RTL of MEALY_TEST is signal STATE,NEXTSTATE : STATE_TYPE ; begin
REG: · · · -- clocked STATE process CMB: · · · -- Like Medvedev and Moore Examples -- Concurrent signal assignments for outputs
Y <= ‘1’
when (STATE = MIDDLE and (A or B) = ‘0’)
or
(STATE = STOP and (A and B) = ‘0’)
else ‘0’; Z <= ‘1’
when (STATE = START and (A and B) = ‘1’)
or (STATE = MIDDLE) or
(STATE = STOP and (A or B) = ‘1’)
else ‘0’; end RTL ;

## Slide 21: Mealy Example Waveform
(Y,Z) changes with input => Mealy machine
Note the "spikes" of Y and Z in the waveform

## Slide 22: Modeling Aspects
Medvedev is too inflexible
  but less hardware (no combinational circuit for output)
  More effort to calculate state vector.
Moore is preferred because of safe operation
  since o/p depends only on state vector.
   next output values are stable long before the next clock edge.
Mealy more flexible, but danger of
  Spikes
  Unnecessary long paths (maximum clock period)
  Combinational feed back loops

## Slide 23: Registered Output
Avoiding long paths and combinational loops.
With one additional clock period
Without additional clock period

## Slide 24: Registered Output Example (1)
architecture RTL of REG_TEST is signal Y_I , Z_I : std_ulogic ; signal STATE,NEXTSTATE : STATE_TYPE ; begin
REG: · · · -- clocked STATE process CMB: · · · -- Like other Examples OUTPUT: process (STATE, A, B) begin case STATE is when START => Y_I<= '0' ; Z_I<= A and B ; · · · end process OUTPUT -- clocked output process OUTPUT_REG: process(CLK) begin if CLK'event and CLK='1' then Y <= Y_I ; Z <= Z_I ; end if ; end process OUTPUT_REG ; end RTL ;

## Slide 25: Reg. Output Example Waveform
One clock period delay between STATE and output changes.
Input changes with clock edge result in an output change. (Danger of unmeant values )

## Slide 26: Registered Output Example (2)
architecture RTL of REG_TEST2 is signal Y_I , Z_I : std_ulogic ; signal STATE,NEXTSTATE : STATE_TYPE ; begin
REG: · · · -- clocked STATE process CMB: · · · -- Like other Examples OUTPUT: process ( NEXTSTATE , A, B) begin case NEXTSTATE is when START => Y_I<= '0' ; Z_I<= A and B ; · · · end process OUTPUT OUTPUT_REG: process(CLK) begin if CLK'event and CLK='1' then Y <= Y_I ; Z <= Z_I ; end if ; end process OUTPUT_REG ; end RTL ;

## Slide 27: Reg. Output Example Waveform
No delay between STATE and output changes.
"Spikes" of original Mealy machine are gone!