## Slide 1: Computer-Aided Design Memory
Some slides courtesy of:
“Hardware Systems Modeling”, A. Vachoux, EPFL
CAD slides from Dr. Saheb Zamani
Mahdi Aminian

## Slide 2: Memory
Memory
CS (Chip-Select)
WrEn
CLK
Address
DataIn
RdEn
DataOut1

## Slide 3: Memory Implementation - 1
Simple DataOut
Library IEEE; use IEEE.Std_Logic_1164.all;
use IEEE.numeric_std.all;
entity Memory1 is
generic( AddrWidth : integer := 8;
DataWidth : Integer := 8 );
port ( CLK : in std_logic;
CS, WrEn, RdEn : in std_logic;
Addr : in std_logic_vector (AddrWidth-1 downto 0); DataIn : in std_logic_vector (DataWidth-1 downto 0);
DataOut1 : out std_logic_vector (DataWidth-1 downto 0) ); end Memory1;

## Slide 4: Memory Implementation - 1
Simple DataOut
architecture RTL of Memory1 is Type MyMem is array (2** AddrWidth -1 downto 0) of std_logic_vector (DataWidth -1 downto 0);
signal Mem : MyMem;
begin
process (CLK) begin
if CLK`event and CLK = `1` then
if (CS = ‘1’ and WrEn = ‘1’) then Mem(to_integer(unsigned(Addr))) <= DataIn; end if; end if; end process;
DataOut1 <= Mem(to_integer(unsigned(Addr)));
end A;

## Slide 5: Memory - 2
Memory
CS (Chip-Select)
WrEn
CLK
Address
DataIn
RdEn
DataOut2

## Slide 6: Memory Implementation - 2
Buffered DataOut
architecture RTL of Memory1 is Type MyMem is array (2** AddrWidth -1 downto 0) of std_logic_vector (DataWidth -1 downto 0);
signal Mem : MyMem;
begin
process (CLK) begin
if CLK`event and CLK = `1` then
if (CS = ‘1’ and WrEn = ‘1’) then Mem(to_integer(unsigned(Addr))) <= DataIn; end if;
end if; end process;
DataOut2 <= Mem(to_integer(unsigned(Addr))) when (CS = ‘1’ and RdEn = ‘1’)
else (others => ‘Z’);
end A;

## Slide 7: Memory - 3
Memory
CS (Chip-Select)
WrEn
CLK
Address
DataIn
RdEn
DataOut3

## Slide 8: Memory Implementation - 3
Registered DataOut
architecture RTL of Memory1 is Type MyMem is array (2** AddrWidth -1 downto 0) of std_logic_vector (DataWidth -1 downto 0);
signal Mem : MyMem;
begin
process (CLK) begin
if CLK`event and CLK = `1` then
if (CS = ‘1’ and WrEn = ‘1’) then Mem(to_integer(unsigned(Addr))) <= DataIn; end if;
if (CS = ‘1’ and RdEn = ‘1’) then DataOut3 <= Mem(to_integer(unsigned(Addr))); end if;
end if; end process;
end A;

## Slide 9: Memory - 4
Memory
CS (Chip-Select)
WrEn
CLK
Address
RdEn
Data

## Slide 10: Memory Implementation - 4
InOut Data
Library IEEE; use IEEE.Std_Logic_1164.all;
use IEEE.numeric_std.all;
entity Memory1 is
generic( AddrWidth : integer := 8;
DataWidth : Integer := 8 );
port ( CLK : in std_logic;
CS, WrEn, RdEn : in std_logic;
Addr : in std_logic_vector (AddrWidth-1 downto 0); Data : inout std_logic_vector (DataWidth-1 downto 0);
); end COUNTER;

## Slide 11: Memory Implementation - 4
InOut Data
architecture RTL of Memory1 is Type MyMem is array (2** AddrWidth -1 downto 0) of std_logic_vector (DataWidth -1 downto 0);
signal Mem : MyMem;
begin
process (CLK) begin
if CLK`event and CLK = `1` then
if (CS = ‘1’ and WrEn = ‘1’) then Mem(to_integer(unsigned(Addr))) <= Data; end if;
end if; end process;
Data <= Mem(to_integer(unsigned(Addr))) when (CS = ‘1’ and RdEn = ‘1’)
else (others => ‘Z’);
end A;

## Slide 12: Case Study Memory Controller

## Slide 13: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  دستگاههاي روي باس با اعلان bus idي mem_buffer (F3) دسترسي به باس را آغاز مي كنند.

## Slide 14: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  يك سيكل بعد, READ_WRITE = ‘1’ مي شود تا بگويد كه يك خواندن مي خواهد انجام شود (يا ‘0’ براي نوشتن).

## Slide 15: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  براي خواندن ممكن است 4كلمه اي (burst read)باشد: بايد در مدت اولين سيكل, burst فعال باشد.

## Slide 16: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  كنترلر به 4 محل از بافر دسترسي مي يابد (به محلهاي بعدي بعد از فعال كردنهاي متوالي ready دسترسي مي يابد).

## Slide 17: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  كنترلر oe را براي mem_buffer در طول خواندن فعال مي كند و دو بايت پايين آدرس را در حالت burst افزايش مي دهد.

## Slide 18: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  نوشتن هميشه يك كلمه اي است.

## Slide 19: Memory Controller
FSM
SRAM
Memory
Array
Address
Data
OE
WE
ADDR1
ADDR0
BUS_ID
Reset
READY
BURST
READ_WRITE
CLK
  هنگام نوشتن we فعال مي شود و data در محلaddress نوشته مي شود.
  خواندن و نوشتن با اعلان ready خاتمه مي يابد.

## Slide 20: Memory Controller
idle
Decision
Write
read1
read2
read3
read4
ready
Read_write
Read_write
ready
ready
. burst
ready
ready
ready
. burst
ready
synch reset
state
ready
  براي همة حالتها مفروض است

## Slide 21: VHDL Code (2-process)
library ieee;
use ieee.std_logic_1164.all;
entity memory_controller is
port (
reset, read_write, ready, burst, clk : in std_logic;
bus_id : in std_logic_vector(7 downto 0);
oe, we : out std_logic;
addr : out std_logic_vector(1 downto 0));
end memory_controller;
architecture state_machine of memory_controller is
type StateType is (idle, decision, read1, read2, read3, read4, write);
signal present_state, next_state : StateType;

## Slide 22: VHDL Code
begin
state_comb:process(bus_id, present_state, burst, read_write, ready)
begin
oe <= ‘0’; we <= ‘0’; addr <= “00”;
next_state <= present_state;
if (ready = ‘0’) then
next_state <= present_state;
else
case present_state is
when idle => oe <= '0'; we <= '0'; addr <= "00";
if (bus_id = “11110011”) then
next_state <= decision;
end if;
when decision=> oe <= '0'; we <= '0'; addr <= "00";
if (read_write = '1') then
next_state <= read1;
else --read_write='0'
next_state <= write;
end if;
In every case, a signal must be assigned to the outputs; otherwise, unwanted latches.

## Slide 23: VHDL Code
when read1 => oe <= '1'; we <= '0'; addr <= "00";
if (burst = '0') then
next_state <= idle;
else
next_state <= read2;
end if;
when read2 => oe <= '1'; we <= '0'; addr <= "01";
next_state <= read3;
when read3 => oe <= '1'; we <= '0'; addr <= "10";
next_state <= read4;
when read4 => oe <= '1'; we <= '0'; addr <= "11";
next_state <= idle;
when write => oe <= '0'; we <= '1'; addr <= "00";
next_state <= idle;
end case;
end if;
end process state_comb;

## Slide 24: VHDL Code
state_clocked: process(clk, reset)
begin
if (reset = '1') then
present_state <= idle;
elsif rising_edge(clk) then
present_state <= next_state;
end if;
end process state_clocked;
end;

## Slide 25: توليد خروجيها در ماشينهاي Moore
  3) خروجيهايي كه مستقيماً در بيتهاي حالت انكد شده اند (Medvedev)
  (مانند شمارنده ها):
Next-State Logic
State Registers
Inputs
Next-State
Current-State
outputs
  State encoding بايد به دقت انجام شود.
  FFهاي بيشتري لازم دارد.
  براي خروجي به مدار ترکيبي نياز ندارد (سرعت بيشتر).

## Slide 26: State Encoding
Addr(0) | Addr(1) | 
0 | 0 | Idle
0 | 0 | decision
0 | 0 | Read1
1 | 0 | Read2
0 | 1 | Read3
1 | 1 | Read4
0 | 0 | Write
s2 | s1
0 | 0
1 | 0
0 | 1
x | x
x | x
x | x
1 | 1
0
0
0
0
0
0
  فرض: فقط براي addr اين كار را انجام مي دهيم (براي we و oe مشكل زماني نداريم)

## Slide 27: State Encoding
Addr(0) | Addr(1) | 
0 | 0 | Idle
0 | 0 | decision
0 | 0 | Read1
1 | 0 | Read2
0 | 1 | Read3
1 | 1 | Read4
0 | 0 | Write
  اگر براي we و oe هم بخواهيم به همين صورت encode کنيم:
we | oe
0 | 0
0 | 0
0 | 1
0 | 1
0 | 1
0 | 1
1 | 0
s0
0
1
0
0
0
0
0

## Slide 28: VHDL Code
architecture state_machine of memory_controller is
-- state signal is a std_logic_vector rather than an enumeration type
signal state : std_logic_vector(4 downto 0);
constant idle : std_logic_vector(4 downto 0) := "00000";
constant decision: std_logic_vector(4 downto 0) := "00001";
constant read1 : std_logic_vector(4 downto 0) := "00100";
constant read2 : std_logic_vector(4 downto 0) := "01100";
constant read3 : std_logic_vector(4 downto 0) := "10100";
constant read4 : std_logic_vector(4 downto 0) := "11100";
constant write : std_logic_vector(4 downto 0) := "00010";
begin
state_comb:process(bus_id, present_state, burst, read_write, ready) …….
state_clocked: process(clk, reset) …….
-- outputs associated with register values
we <= state(1);
oe <= state(2);
addr <= state(4 downto 3);
end state_machine;